## Slide 1: Introduction to Computer Networks The OSI and TCP/IP Models
120CT Computer Architecture and Networks
Dr Dianabasi Nkantah
ab0480@coventry.ac.uk

## Slide 2: This lecture ……
Introduction to Computer Networks
The OSI Model
The TCP/IP Model

## Slide 3: Introduction to Computer Networks
Discover what a network is
Understand the need for layers in Networked computing
Understand the OSI model
Look at the different layers in the OSI model
Look at the different layers in the TCP/IP model

## Slide 4: Networks in Our Past and Daily Lives
Notes: Section 1.1.1.1 & 1.1.1.2

## Slide 5: What is a network?
A computer network links two or more pieces of hardware.
The hardware need not be in the same location.

## Slide 6: Applications of networks
What are the applications of computer networks?

## Slide 7: LANs, WANs, and Internets Components of a Network
There are three categories of network components:
Devices
Media
Services
Notes: Section 1.2.1.1

## Slide 8: What are networks made up of?
Cables
Wireless
Routers
Computers
Phones
Tablets
Firewalls
Protocols
Users
Satellite communication
Printers
Monitors
Etc ..

## Slide 9: Layering in network computing
Breaks down communication into smaller, simpler parts
  Speeds development, changes in one layer does not affect how the other levels works.
  Standardisation across manufacturers.
  Allows different hardware and software to work together.
  Reduces complexity

## Slide 10: OSI Model
OSI “Open Systems Interconnection".
OSI model was first introduced in 1984 by the International Organization for Standardization (ISO).
  Outlines what is required to send data from one computer to another.
  Not how to do it.
In the OSI model, the details are included in 7 different layers that interact with each other.

## Slide 11: OSI Model
Plan to assist the understanding of how data passes from one device to another
Assists in the creation of standards so hardware and software can communicate
Assists in the standardisation of networking technologies by providing a structure for hardware and software developers to follow

## Slide 13
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Model
Provides user applications access to network resources

## Slide 14
Application
Presentation
Session
Transport
Network
Data Link
Physical
  Formats data for passing between points of communication
OSI Model

## Slide 15
Application
Presentation
Session
Transport
Network
Data Link
Physical
The session layer offers the approach to managing a session between user application processes
OSI Model

## Slide 16
Application
Presentation
Session
Transport
Network
Data Link
Physical
logical communication between processes
OSI Model

## Slide 17
Application
Presentation
Session
Transport
Network
Data Link
Physical
logical communication between hosts
OSI Model

## Slide 18
Application
Presentation
Session
Transport
Network
Data Link
Physical
The data link layer transfers data across physical media
OSI Model

## Slide 19
Application
Presentation
Session
Transport
Network
Data Link
Physical
Handles the passing 0s and 1s over the physical media as a signal

## Slide 20
Application
Presentation
Session
Transport
Network
Data Link
Physical
A- Write a 10 page letter in English to someone in France.
P- Translate the letter so the receiver can read it.
S- Ensure the intended recipient can receive letter.
T- Separate and number pages. Like registered mail, tracks delivery and requests another package if one is “lost” or “damaged” in the mail.
N- Postal Center sorting letters by post code to route them closer to destination.
D- Local Post Office determining which vehicles to deliver letters.
P- Physical Trucks, Planes, Rail, autos, etc which carry letter between stations.

## Slide 21: Presentation layer
Determines the format used to exchange data among networked computers.
Translates data from a format from the Application Layer into an intermediate format.
Responsible for protocol conversion, data translation, data encryption, data compression, character conversion, and graphics expansion.
Data coming in from another computer is translated and served up to the presentation layer. Data coming down from the Presentation Layer is encoded for transfer down.

## Slide 22: Session Layer
This layer allows two applications running on different computers to connect.
When the two applications are communicating, it handles that communication, and terminates it when complete.
This is done by establishing sessions, which a port number is assigned to.

## Slide 23: Example - Transport layer

## Slide 24: Transport Layer
provide logical communication between app processes running on different hosts
transport protocols run on end systems
  send side: breaks app messages into segments, passes to network layer
  receive side: reassembles segments into messages, passes to app layer

## Slide 25: Transport vs. Network Layer University internal mail
Host
Host
Processes
Processes
network-layer protocol
Messages
Transport-layer protocol
Transport-layer protocol

## Slide 26: Transport layer - Congestion Control
What it is:
  informally: “too many sources sending too much data too fast for network to handle”
Manifestations:
  Lost packets and delays
Congestion Control:
  Decrease load
  Increase the resources
Notes: Symptoms:

## Slide 27: Encapsulation in OSI model
Header: Identifies the protocol in use, the sender and intended recipient
Tail: Provides data integrity checks

## Slide 28: A data journey
Scenario
You are playing an online game, and you move forward one step.
This move has to be sent over the network to the game server.
The data that your game uses to denote the move is sent down from the Application Layer to the Presentation Layer.
There it gets checked to make sure it is in the right format, or encrypt it if that has been requested.

## Slide 29: A data journey
From there, it is sent down to the Session Layer, at which point it is sent to the Port allocated to this application (your game) to be sent to the game server.
Now the data arrives at the Transport Layer. Even such a small piece of data as a game move instruction might be too big to be sent all in one go.

## Slide 30: A data journey
Therefore the Transport Layer breaks the data up into packets, giving them the previously mentioned local and destination addresses, and numbering them so they can be reassembled in the right order when they arrive.
These packets are sent down to the Network Layer. They addresses are read, and a check is made to see whether the destination host is reachable (whether it is online still). If it is, then the packets are passed down to the Data Link Layer.

## Slide 31: A data journey
The Data Link Layer takes the packets representing your move, and translates them into a form the physical network hardware can understand, and send it down to the Physical layer.
The Physical Layer then sends the data out onto the network, a packet at a time.
These packets are then received by the Physical Layer of the destination computer, and sent up to the Data Link Layer.

## Slide 32: A data journey
The Data Link Layer converts the data from the Physical Layer form into the Packet form which can be recognised by the Network Layer, and sent up to it.
The Network Layer checks the packets it has received from the Data Link Layer to make sure they are undamaged, and when it has received all the packets which are likely to arrive it checks to see if any are missing. If any are, or are damaged, then request are sent back down to the Data Link Layer for replacements to be sent.

## Slide 33: A data journey
Assuming everything has arrived, the packets are sent up to the Transport Layer, where they are reassembled into a single contiguous block of data again.
From there it is sent up to the Presentation Layer, where it is checked to make sure that it conforms to the right data type, and unencrypted if required.

## Slide 34: A data journey
The Presentation Layer then send the data up to the Application Layer, where it is sent to the correct receiving program, and your player character is moved forward by the specified amount.

## Slide 35: So far, we have seen that ….
Networking involves the connection of devices and the passing of data
This is best achieved by using a layered approach
We looked at one such approach the OSI
We worked through the process involved in passing data

## Slide 36: The TCP/IP Model
Any device on the Internet that wants to communicate with other Internet devices must have a unique logical identifier.
The identifier is known as the IP address or logical address. It is used by routers to find the best route to that device.
The current version of IP is IPv4.
    Subnets, Network Address Translation (NAT) and private addresses are used to extend the supply of IP addresses
IPv6 improves on IPv4 and provides a much larger address space.
Notes: Any device on the Internet that wants to communicate with other Internet devices must have a unique identifier. The identifier is known as the IP address because routers use a Layer 3 protocol called the IP protocol to find the best route to that device. The current version of IP is IPv4. This was designed before there was a large demand for addresses. Explosive growth of the Internet has threatened to deplete the supply of IP addresses. -----Subnets,
--Network Address Translation (NAT), and
---private addresses
are used to extend the supply of IP addresses.
IPv6 improves on IPv4 and provides a much larger address space. Administrators can use IPv6 to integrate or eliminate the methods used to work with IPv4.
For efficient routing to occur between devices, issues such as duplicate IP addresses must be resolved.

## Slide 37: The TCP/IP Layered model
Application
Transport
Internet
Network Access
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Model
Notes: The four layers of the TCP/IP model are:
the application layer,
transport layer,
Internet layer, and
network access layer.
Some of the layers in the TCP/IP model have the same name as layers in the OSI model. It is critical not to confuse the layer functions of the two models because the layers include different functions in each model.

## Slide 38: The TCP/IP Layered model Application Layer
Application
Transport
Internet
Network Access
Handles high-level protocols, representation, encoding, and dialog control.
Supports file transfer, e-mail, remote login, network and name management.
Protocols: DNS, SNMP, Telnet, SMTP, NFS, FTP, TFTP
Notes: The application layer handles high-level protocols, representation, encoding, and dialog control.
The TCP/IP protocol suite combines all application related issues into one layer. It ensures that the data is properly packaged before it is passed on to the next layer.
TCP/IP includes Internet and transport layer specifications such as IP and TCP as well as specifications for common applications. TCP/IP has protocols to support file transfer, e-mail, and remote login, in addition to the following:
  File Transfer Protocol (FTP) – FTP is a reliable, connection-oriented service that uses TCP to transfer files between systems that support FTP. It supports bi-directional binary file and ASCII file transfers.
  Trivial File Transfer Protocol (TFTP) – TFTP is a connectionless service that uses the User Datagram Protocol (UDP). TFTP is used on the router to transfer configuration files and IOS images, and to transfer files between systems that support TFTP. It is useful in some LANs because it operates faster than FTP in a stable environment.
  Network File System (NFS) – NFS is a distributed file system protocol suite developed by Sun Microsystems that allows file access to a remote storage device such as a hard disk across a network.
  Simple Mail Transfer Protocol (SMTP) – SMTP administers the transmission of e-mail over computer networks. It does not provide support for transmission of data other than plain text.
  Telnet – Telnet provides the capability to remotely access another computer. It enables a user to log into an Internet host and execute commands. A Telnet client is referred to as a local host. A Telnet server is referred to as a remote host.
  Simple Network Management Protocol (SNMP) – SNMP is a protocol that provides a way to monitor and control network devices. SNMP is also used to manage configurations, statistics, performance, and security.
  Domain Name System (DNS) – DNS is a system used on the Internet to translate domain names and publicly advertised network nodes into IP addresses.

## Slide 39: The TCP/IP Layered model Transport Layer
Application
Transport
Internet
Network Access
Provides transport services from the source host to the destination host.
Protocols:
TCP (Transmission Control Protocol) which is connection oriented.
UDP (User Datagram Protocol) which is connectionless.
Notes: The transport layer provides a logical connection between a source host and a destination host.
Transport protocols segment and reassemble data sent by upper-layer applications into the same data stream, or logical connection, between end points.
Transport layer protocols include TCP and UDP.
The functions of TCP and UDP are as follows:
Segment upper-layer application data
Send segments from one end device to another
The functions of TCP are as follows:
Establish end-to-end operations
Provide flow control through the use of sliding windows
Ensure reliability through the use of sequence numbers and acknowledgments

## Slide 40: The TCP/IP Layered model Internet Layer
Application
Transport
Internet
Network Access
Best path determination and packet switching occur at this layer.
The purpose of this layer is:
the selection of the best path for packets to travel.
Routing of packets to remote hosts
Main protocol: IP
Notes: The purpose of the Internet layer is to select the best path through the network for packets to travel. The main protocol that functions at this layer is IP. Best path determination and packet switching occur at this layer.

## Slide 41: The TCP/IP Layered model Network Access Layer
Application
Transport
Internet
Network Access
Allows an IP packet to make a physical link to the network media.
Map IP addresses to physical hardware addresses and encapsulate IP packets into frames.
Defines the physical media connection based on the hardware type and network interface.
Notes: The network access layer allows an IP packet to make a physical link to the network media.
It includes the LAN and WAN technology details and all the details contained in the OSI physical and data link layers.
Network access layer protocols also map IP addresses to physical hardware addresses and encapsulate IP packets into frames.
The network access layer defines the physical media connection based on the hardware type and network interface.

## Slide 42: Address Schemes IPv4 (32 Bit) IPv6(128 Bit)
Notes: 2.2.3 Hostnames

## Slide 43
Internetwork connection is made possible using a logical addressing scheme within the Internet layer (OSI layer 3), known as IP addressing
The IP address consists of a 32-bit binary number, divided into four 8-bit segments called octets
For ease of use, the IP address is usually represented in a dotted decimal notation, with each octet given as a decimal number:
209.121.131.14
Octet
IP Addressing
Notes: With IPv4 hierarchical addressing, the network portion of the address for all hosts in a network is the same. To divide a network, the network portion of the address is extended to use bits from the host portion of the address. These borrowed host bits are then used as network bits to represent the different subnetworks within the range of the original network.
Given that an IPv4 address is 32 bits, when host bits are used to divide a network the more subnetworks created results in fewer hosts for each subnetwork. Regardless of the number of subnetworks created however, all 32 bits are required to identify an individual host.
Quickly recap some binary:
Octet = 8-bits = Byte
64 32 16 8 4 2 1
1 1 1 1 1 1 1 1
What is the minimum number possible?
0
What is the maximum number possible?
255

## Slide 44: Internet Protocol Version 6
Starting to be deployed – running in parallel with IPv4.
Uses a 128-bit address length, written in hexadecimal:
2031:0:130F:0:0:9C0:876A:130B.
Provides 3.403 x 1038 addresses (2128).
Provides sufficient address space to satisfy foreseeable Internet expansion.

## Slide 45: Ports and Addresses IP Addressing in the Large
Each end device on a network must be configured with an IP address
Structure of an IPv4 address is called dotted decimal
IP address displayed in decimal notation, with four decimal numbers between 0 and 255
With the IP address, a subnet mask is also necessary
IP addresses can be assigned to both physical ports and virtual interfaces
Notes: 2.3.1.1 IP Addressing in the Large

## Slide 46
Additional Reading Resources