## Slide 1: Functional Units from Logic Gates (Combinational Circuits)
120CT Computer Architecture & Networks
Dr Dianabasi Nkantah
ab0480@coventry.ac.uk

## Slide 2: Functional Units from Logic gates
Decoders
Encoders
Multiplexers
Comparators
Special use of the X-OR gate
Adder circuits
    Full adder
    4 bit adder
Arithmetic and Logic Unit
  Arithmetic unit
  Addition
  2’s complement subtraction
  Logic unit
  Tri-state

## Slide 3: Combinational Circuits
A combinational circuit is an interconnected set of gates
  Its output at any time is a function of the inputs at that time
A combinational circuit can be defined in three ways:
  Truth table
  Graphical symbols
  Boolean equations
Examples of Combinational Circuits that are functional units in a computer:
  Decoders, Encoders, Multiplexers, Demultiplexers, Comparators, Adders

## Slide 4
A decoder is a logic circuit that detects the presence of a specific combination of bits at its input.
Decoders

## Slide 8
Decoders
Applications:
Instruction Decoding
Input/Output Selection
BCD-to-Decimal Decoding
Address decoding
Notes: A 3-to-8 line decoder is also known as a 1-in-8 decoder. A 4-to-16 line decoder is also known as a 1-in-16 decoder.

## Slide 9
Applications:
Decimal-to-BCD Decoding
Assemblers (Software encoders)
An encoder accepts an active logic level on one of its inputs and converts it to a coded output, such as BCD or binary.
Encoders

## Slide 10
Application:
Control of access to a shared bus by processors on a multi-processor system (Bus Arbiter)
A multiplexer (MUX) selects one data line from two or more input lines and routes data from the selected line to the output. The particular data line that is selected is determined by the select inputs.
Multiplexers

## Slide 11
Comparators
The function of a comparator is to compare the magnitudes of two binary numbers to determine the relationship between them. In the simplest form, a comparator can test for equality using XNOR gates.
Example
How could you test two 4-bit numbers for equality?
Solution
AND the outputs of four XNOR gates.
A2
B2
A3
B3
A4
B4
A1
B1
Output

## Slide 12
Schematic diagram of the half adder
T
B
S
Cout
(Sum)
(Carry out)
EOR
AND
 | T
 | + B
Cout | S
1-bit addition
Truth Table |  |  | 
T | B | S | Cout
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Half-Adder

## Slide 18
Notes: To add two binary numbers (each with multiple bits), a multiple-bit parallel full-adder (combination of multiple full-adders) is required. For example, to add two 4-bit numbers, a 4-bit parallel adder is required. To add two 16-bit numbers, a 16-bit parallel adder is required.

## Slide 30: Further Reading
Computer Organization and Architecture – Designing for Performance (10th Edition), William Stallings [Chapter: 11]
Digital Fundamentals (11th Edition), Thomas L. Floyd [Chapter: 6]
Computer Organization and Design – The Hardware/Software Interface (5th Edition), David A. Patterson & John L. Hennessy [Appendix: A]
Fundamentals of Computer Architecture, Mark Burrell [Chapter: 4, 5]

## Slide 31: Next Class ….
Introduction to Sequential Logic
  Latches and Flip-flops
    set, reset
    truth table
    clocked latch,
    edge triggered FF
      timing diagram, operation
      D-type FF
      clear & preset
      toggles
Counters
Shift Registers